## Slide 1: Project 12 Mathematical Reconstruction of Patient-Specific Vascular Network Based on Clinical Images and Global Optimization
Students: Yifan Jiang1, Abdul Hannan Faruqi2, Junhong Shen3
Supervisor: Dr. Nima Maftoon (University of Waterloo)
1 University of Toronto
2 Aligarh Muslim University
3 University of California, Los Angeles

## Slide 2: Motivation
Modelling tumor growth and its vascularization
Blood flow plays a vital role in metastasis.
To study circulating tumor cells in metastasis and the location of secondary tumor sites detailed geometry of vascular network is needed.
Our computational framework is aimed at providing this detailed network structure which could aid in predicting metastasis sites.
Metastasis

## Slide 3: Patient-specific Vascular Network
Brain Angiography
Idealized Brain Vascular Network

## Slide 4: Our Framework
Medical Image Preprocessing
Large Vessel Extraction
Optimization-based Structure Refinement (Global Constructive Optimization)
Volume Generation
Postprocessing
Image-based 3D Vessel Reconstruction with Structure Approximation
Global optimization solved by GCO: merge / split / prune
Local optimization solved by relaxation

## Slide 5: Cost Function: Material Cost
3D Model of Bifurcation

## Slide 6: Cost Function: Power Cost
Power loss during blood circulation

## Slide 7: Cost Function for Relaxation
subject to:
Illustration of MC
Illustration of PC

## Slide 8: Optimization Algorithm: Selection
Gradient-Descent
Follows the gradient to reach the
optimum point
Simulated Annealing
Samples multiple points in the domain
and then narrows down to an optimum
Surrogate-based Modelling
Approximates the actual objective function based
on sampled points and then gives the minimum
Cost Change for GD
Source: Hands-on Machine Learning - O’Reilly
Cost Change for SM
Source: ResearchGate - Erich Wehrle
Cost Change for SA
Source: Wikipedia

## Slide 9: Optimization Algorithm
Simulated Annealing
An optimization method inspired by annealing process in metallurgy.
Has high probability of acceptance in the beginning and it decreases with temperature (iterations).
Finds the global optimum when there are multiple local optima.
Simulated Annealing Example
Source: Wikipedia

## Slide 10: Optimization Algorithm: Results
Finding the global minimum using simulated annealing.
Locations of Points sampled
Change of Cost Function

## Slide 11: Optimization Algorithm: Parameters
Important parameters for Simulated Annealing:
Temperature (Chosen value = 1)
  It defines the acceptance probability of a bad move. (Good moves are always accepted)
Cooling coefficient (Chosen value = 0.999)
It affects the ability to reach equilibrium
Move Function (Function = [-1, 1] * 0.005 * range)
It defines the ability of exploring the domain

## Slide 12: GCO Implementation (2D)
GCO Algorithm
(1) Initialization
(2) Split
(3) Prune and Reconnect
(4) Result

## Slide 13: GCO Implementation (3D)
(4) Result
(2) Split
GCO in 3D
(1) Initialization
(3) Relax

## Slide 14: Locate Fixed Nodes: Extract Main Vessels
Brain vessel segmentation from angiography using NiftyNet
3D Brain Angiography
Segmented Vessel Mesh

## Slide 15: Locate Fixed Nodes: Extract Main Vessels
Voxelize: mesh -> 3D binary array
Connected component analysis: obtain two main vessels
Voxel Representation of Vessels
Voxel Representation of Main Vessel Parts

## Slide 16: Locate Fixed Nodes: Node and Edge Representation
Sample points (coordinates) from the vessels to retain the main structure of the network
Node and Edge Representation of Main Vessels

## Slide 17: Sample Leaf Nodes: Parametrization
Brain Model Without Parametrization
Brain Model With Parametrization

## Slide 18: Sample Leaf Nodes: Approach
Take 512 slices and fit the curve with several mathematical expression.
Polynomial fit:
Ellipse fit:
Circle fit:

## Slide 19: Sampling Algorithm: Region of Influence
Randomly sample some points in the domain and define a region of influence around each point
Rearrange the points to fill unsupplied regions
The Algorithm:
  Find misses
  Find overlaps + outliers
  Move these points to missed regions
  Add more points, if needed
Region of Influence Example
Source: ScienceDirect - C.Pozrikidis, J.M.Davis

## Slide 20: GCO Forest on Brain Vascular Network
Connect leaf nodes with nearest fixed nodes
Fixed node number: 1099
Leaf node number: 3016
GCO Forest Initialization

## Slide 21: GCO Forest: Result
GCO Result

## Slide 22: Characterize Trees: Horton-Strahler Order
Example of Strahler Order

## Slide 23: GCO Forest: Result
Vessels with Strahler order > 2
Vessels with Strahler order > 3
GCO Result

## Slide 24: Result Analysis: Validation
Diameter / Branch Length / Strahler Order Frequency
Diameter Distribution
Branch Length Distribution
Strahler Order Distribution

## Slide 25: Result Analysis: Validation
Inverse Square Root of Diameter / Log Branch Length
Distribution of
Distribution of

## Slide 26: Result Analysis: Validation
Strahler Order v.s. Mean Diameter / Mean Branch Length
Mean Diameter for each HS order
Mean Branch Length for each HS order

## Slide 27: Analysis: 3D Visualization of Final Model
Reconstructed 3D Brain Model

## Slide 28: Analysis: Blood Flow Modelling
Mesh generation
Geometry needs some cleansing before performing actual calculations
Aim: model the flow to get pressure distribution and wall shear stress and compare it with actual data
Reconstructed Vessel Model

## Slide 29: Future Work
Further modelling of blood flow and shear stress
Incorporate vesselness map into Simulated Annealing algorithm
Incorporate more physiological properties into the cost function

## Slide 30: Acknowledgements
Special thanks to the Fields Institute for organizing the program
We feel deeply indebted to our supervisor Dr. Nima Maftoon and his PhD student Sina Anvari Naeini for guiding us through the course of this project

## Slide 31
Thank You!